## Slide 1
MODULE BIOMECHANICS OF GAIT
Didactic Unit D: INSTRUMENTED ANALYSIS OF GAIT
D.1 Which gait biomechanical instrumented evaluation protocols exist?

## Slide 2
Part 1 Photogrammetry
Part 2 Accelerometers
Part 3 Dynamometric platforms
Part 4 Instrumented pressure insoles
Keys ideas
Bibliography
D.1 Which gait biomechanical instruments evaluation protocols exist?
Notes: This presentation has animations in the text and images. Pay attention to the animations during the presentation.

## Slide 3
D.1 Which gait biomechanical instruments evaluation protocols exist?
Part 1. Photogrammetry and gait assessment.
Clinical approach

## Slide 4
Photogrammetry is the science of obtaining reliable information about the properties of surfaces and objects without physical contact with the objects, and of measuring and interpreting this information.
1. DEFINITION
Video camera
or
Photo camera
Images
Kinematic
variables
Photogrammetry
phot
light
grama
draw
metrein
measure

## Slide 5
2. SYSTEM ELEMENTS
Video camera system and spotlights or lighting system
Image recording and processing system: software
Reference system
Markers and accesories

## Slide 6
Light effect
Figure 1. Smartcam from movement capture system kinescan/IBV
2.1. SYSTEM ELEMENTS: CAMERAS

## Slide 7
2.1. SYSTEM ELEMENTS: CAMERAS
Notes: Kinescan / IBV movement analysis system. Institute of Biomechanics Valencia Spain.

## Slide 8
versus
Figure 2. Configuration of cameras for analysis in two-dimensions versus three-dimensions. Medicine Department Lab. University of Valencia
2.1. SYSTEM ELEMENTS: CAMERAS

## Slide 9
Configurations for camera-based motion capture
Two-dimensional system
One camera
Coronal or sagittal
plane movement
Positioned orthogonally
to capture
Figure 3. Two-dimensional video
camera configuration
2.1. SYSTEM ELEMENTS: CAMERAS

## Slide 10
Figure 4. Linear camera configuration
Figure 5. Umbrella camera configuration
Configurations for camera-based motion capture
Three-dimensional system
2.1. SYSTEM ELEMENTS: CAMERAS

## Slide 11
Recording frequencies per second with photogrammetry system |  |  | 
Author | Motor task | Frecuency | Sample
Martin S. et al. 2014 | Gait | 75 Hz | Healthy participants
Jeremy J.B. et al. 2007 | Gait | 120 Hz | Normally active girls
Bisesti et al. 2015 | Running | 240 Hz | Healthy participants
Huchez et al. 2013 | Gymnastics | 250 Hz | Athletes
Inoue et al., 2014 | Soccer | 500 Hz | Athletes
Betzler et al. 2014 | Golf | 1000 Hz | Athletes
2.1. SYSTEM ELEMENTS: CAMERAS
Table 1. Recording frequencies (Hz) with motion capture system.

## Slide 12
2.2. SYSTEM ELEMENTS: SOFTWRE
Images recording
Images processing
Figure 6. Motion capture system software available in the market

## Slide 13
2.3. SYSTEM ELEMENTS: REFERENCE SYSTEM
Global coordinate system (GCS)
STATIC CALIBRATION
DYNAMIC CALIBRATION

## Slide 14
Static calibration
1 m
1 m
Two-dimension
2.3. SYSTEM ELEMENTS: REFERENCE SYSTEM
Figure 7. Rigid cubic structure for static space calibration in two-dimensional analysis

## Slide 15
Static calibration
1 m
1 m
1 m
1 m
Three-dimension
2.3. SYSTEM ELEMENTS: REFERENCE SYSTEM
Figure 8. Rigid cubic structure for static space calibration in three-dimensional analysis

## Slide 16
Dynamic calibration
2.3. SYSTEM ELEMENTS: REFERENCE SYSTEM
Figure 9. Dynamic space calibration with a wand and tracking cloud

## Slide 17
2.4. SYSTEM ELEMENTS: MARKERS AND ACCESORIES
Markers
Passive markers
Figure 10. Passive individual markers
Figure 11. Passive cluster markers
Scotchlite reflective material

## Slide 18
Markers and other materials
Active markers
Other materials
Figure 12: Active markers
(Image from J. Richards et al. 2018)
Figure 13: Double-contact adhesive
2.4. SYSTEM ELEMENTS: MARKERS AND ACCESORIES
Notes: Hypoallergenic adhesive
Dermographic pencil
Shaver
Alcohol and gauze
Appropriate clothing
Tie raps or similar

## Slide 19
3.1. MOVEMENT DEFINITION AND BIOMECHANICAL MODEL
What we want to measure?
versus
Figure 15.Configuration for lower limb gait analysis. From Eng H. Lee et al. 1992
Figure 14. Configuration for ankle movement analysis. From A. Ali and T. Gevers. 2011

## Slide 20
Configurations of biomechanical model for gait analysis
  Head of the fifth metatarsal
  Lateral malleolus
  Lateral condyle of the femur
  Greater trochanter
  Anterior superior iliac spine
  Acromion process
  Lateral condyle of the humerus
  Styloid process at the wrist
It is not possible to measure
axial rotation
Simple marker set
3.1. MOVEMENT DEFINITION AND BIOMECHANICAL MODEL
Figure 16. Simple marker set configuration
Notes: *There are animation effects on this slide

## Slide 21
Configurations of biomechanical model for gait analysis
  Head of the fifth metatarsal
  Lateral malleoli
  Heel
  Tibial tuberosity
  Femoral epicondyle
  Greater trochanter
  Anterior superior iliac spine
  Sacrum
Vaughan Marker set
Functional reference of the foot
Pelvic Tilt
3.1. MOVEMENT DEFINITION AND BIOMECHANICAL MODEL
Figure 17. Vaughan marker set configuration
Notes: *There are animation effects on this slide

## Slide 22
Configurations of biomechanical model for gait analysis
  Head of the second metatarsal
  Lateral malleoli
  Heel
  Tibial wand
  Femoral epicondyle
  Femoral wand
  Greater trochanter
  Anterior superior iliac spine
  Sacrum
Helen Hayes Marker set
Tibial and femoral wands for femoral and tibial rotations.
3.1. MOVEMENT DEFINITION AND BIOMECHANICAL MODEL
Figure 18. Helen Hayes marker set configuration
Notes: *There are animation effects on this slide

## Slide 23
Configurations of biomechanical model for gait analysis
The Calibrate Anatomical System Technique Marker set (CAST)
Standardize the description of the pelvis and lower limb
Six-degrees of freedom
  Three linear or translational movements
  Three rotation or angular movements
Two types of markers: anatomical and segment
3.1. MOVEMENT DEFINITION AND BIOMECHANICAL MODEL

## Slide 24
The Calibrate Anatomical System Technique Marker set (CAST)
Anatomical markers
Used for calibration of the model
Located lateral and media to the joints
Joints instrumented: proximal and distal to the each segment
Global coordinates system  Local coordinates system
3.1. MOVEMENT DEFINITION AND BIOMECHANICAL MODEL

## Slide 25
Global coordinates system
(GCS)
Local coordinates system
(LCS)
Figure 19. Global coordinates system versus Local coordinates system

## Slide 26
The Calibrate Anatomical System Technique Marker set (CAST)
Anatomical markers
Foot segment
Tibial segment
Femoral segment
Pelvis segment
Metatarsal head
Ankle malleolli
Ankle malleolli
Femoral Condyles
Posterior superior iliac
Anterior superior iliac
Femoral Condyles
Greater trochanter
3.1. MOVEMENT DEFINITION AND BIOMECHANICAL MODEL

## Slide 27
The Calibrate Anatomical System Technique Marker set (CAST)
Segment markers
They can be located arbitrarily in the segment
Easily tracked
Non-collinear
At least three markers in each segment
3.1. MOVEMENT DEFINITION AND BIOMECHANICAL MODEL

## Slide 28
3.2. DATA CAPTURE
1º
Static calibration scene
2º
Gait trial
Scene

## Slide 29
What is important during the recording of the gait?
Enough space to make several strides
Gait performance without interference of model instrumentation
Makers must be visible throughout the measurement record
Standardized instruction
3.2. DATA CAPTURE

## Slide 30
3.3. DIGITIZING OF THE MEASURES
Digitizing or tracking is the process of identifying points on the body using markers or a visual impression of the joint centres. There are two methods of digitizing: manual and automatic.
Manual
digitizing
Automatic
digitizing

## Slide 31
Primary results: coordinates on the x, y and z axis of all the markers and frames of the scene.
3.4. OBTAINING THE RESULTS
Calculation of kinematic outcomes from the extracted coordinates
Analysis in relation to the gait cycle (%)
Kinematics and spatiotemporal outcomes
Figure 20. Hip movement analysis related to gait cycle

## Slide 32
Outcomes from photogrammetry system | 
Kinematics | Spatiotemporal
Range of motion Flexo-extension Internal-external rotation Abduction-adduction | Gait velocity (m/s)
 | Stride length (m)
 | Stride time (s)
 | Step length (m)
Peak angle Maximum plantiflexion and dorsiflexion of the ankle Maximum flexion and extension of the knee Maximun extension and flexion of the hip | Step width (m)
 | Cadence (steps / min)
 | Foot angle in stance/swing phase
 | Stance phase duration (s) or (%)
 | Swing phase duration (s) or (%)
 | Double support time (%)
3.4. OBTAINING THE RESULTS
Table 2. Main outcomes from the kinematic analysis

## Slide 33
Range of motion
Maximum dorsalflexion
Maximum plantarflexion
3.4. OBTAINING THE RESULTS
Figure 21. Ankle movement curve in gait cycle. Analysis of the range of motion versus peak angle

## Slide 34
4. ADVANTAGES AND DISADVANTAGES
Detail analysis
Many possibilities
High cost
Qualified staff
Figure 22. Diagram with the characteristics of the photogrammetry system

## Slide 35
Errors associated with the measurement technique
Relative errors: movement between two or more markers
Errors involved with marker placement: soft-tissue artefacts
Absolute errors: movement of a marker with respect to the bony landmark it is representing
4. ADVANTAGES AND DISADVANTAGES

## Slide 36
Errors associated with the measurement technique
Usual with standard video cameras in two-dimensional analysis
Errors related to image distortion
Marker distortion from higher-speed distal segment movement
4. ADVANTAGES AND DISADVANTAGES

## Slide 37
Errors associated with the measurement technique
Errors in estimating the centre of a maker
4. ADVANTAGES AND DISADVANTAGES
Figure 23. Representation of the centroid marker in relation to its size

## Slide 38
Errors associated with the measurement technique
Related to the gait repetitions  standardization of the procedure
Other types of errors
Low external validity  unrepresentative
4. ADVANTAGES AND DISADVANTAGES

## Slide 39
D.1 Which gait biomechanical instruments evaluation protocols exist?
Part 2. Accelerometers and gait assessment.
Clinical approach

## Slide 40
F = m * a
1. DEFINITION
Accelerometers are devices which measure the applied acceleration along an axis.
They are a basic technology that converts mechanical motion into an electrical signal.
Their internal function is based on the inertia of a mass located on a force sensor, following the Second law of Newton to obtain acceleration.
Accelerometers
Figure 1. Second law of Newton.

## Slide 41
1. DEFINITION
Acceleration experienced by the lower limb segments.
Accelerometers in gait
Linear acceleration
m/s2  g (gravity ratio)
Change in the linear velocity over successive time intervals
Acceleration (+)
Deceleration (-)
Figure 2. Acceleration representation of the tibial segment during walking.

## Slide 42
2. SYSTEM ELEMENTS
SENSOR
ANALYZER
AMPLIFIER
Device that measures the acceleration values from the vibration of the body to which is attached.
Device that amplifies the signal received by the accelerometer and sends it to a computer.
It is a computer with the software that receives the acceleration data and allows its subsequent analysis.
Uniaxial
Triaxial

## Slide 43
2. SYSTEM ELEMENTS
Capacitive | Mechanical
Piezoelectric | Piezoresistive
Figure 3.The images show the functioning of the different types of sensors used in an accelerometer device. Images from Woodford, Chris. (2009/2014) Accelerometers.

## Slide 44
Previous consideration
To measure body parts, accelerometers are placed on the body part whose movement is being studied.
3. ASSESSMENT PROTOCOL
To measure whole body movements, multiple instruments are used.
In gait analysis for measure the body segment movement, only need a lower frequency (60-100 Hz) and a smaller range (typically 6-9 g)

## Slide 45
Placement of equipment in the body
Adhesive material
Importance of fixed
  Good fixation will allow that the device represent the acceleration of the underlying bone
  To avoid relative movement of the sensor
  To avoid soft tissue
3. ASSESSMENT PROTOCOL
Figure 4. Elements to fix the accelerometer in the tibia. (A) non-invasive system, (B) invasive system, accelerometer subject to Steinmann pins under the skin. Image from Sinclair et a. (2013) and Lafortune M. et al. (1991)
A
B

## Slide 46
Anatomical placement
HEAD
TRUNK
TIBIAL
3. ASSESSMENT PROTOCOL
  L5 vertebra
  Sacrum
  Forehead
  Posterior region
A
C
Figure 6. Usual accelerometer placement (A) Forehead location. (B) Tibial location in the proximal end and anteromedial area. (C) Tibial location in the distal end for ground impact measurement.
  Forehead
  Posterior region
B

## Slide 47
Obtaining results
Peak
amplitude of
acceleration
  Positive peak
  Negative peak
  Different axes
  Time between peaks
3. ASSESSMENT PROTOCOL
Spatiotemporal
parameters
Figure 7. Head accelerations during gait. Image from Brodie, Matthew A D. et al. (2015).
Time (s)
Acceleration
Positive acceleration
Negative acceleration

## Slide 48
4. ADVANTAGES AND DISADVANTAGES
Advantages
Low cost
Transportable
Disadvantages
Sensitive to shock by large deceleration
Precision alterations due to instability of skin fixation
Real time information
wired system limited the assessment

## Slide 49
D.1 Which gait biomechanical instruments evaluation protocols exist?
Part 3. Dynamometric platforms and gait assessment.
Clinical approach

## Slide 50
1. DEFINITION
Ground Reaction Forces (GRF)
Centre of Pressure (COP)
Dynamometric Platform
Equipment to measure forces
Widely used in the assessment of human gait and balance, as well as in several human activities
Fixed in the ground

## Slide 51
2. SYSTEM ELEMENTS
Figure 1. Bertec force platform of strain gauge
2.1 The Platform
Figure 2. Kistler force platform of piezoelectric sensors
Types of sensors

## Slide 52
2. SYSTEM ELEMENTS
2.1 The Platform
Principal characteristics of piezoelectric and strain gauge platform | 
Strain-gauge | Piezoelectric
Material distorted produce a resistance (strain) | Deformation of the crystal that generate an electric current
Less sensitive, less range of force measurement | More sensitive, large range of force measurement
Frequency of 400-500 Hz | Higher frequency, 1000 Hz in three directions
Adequate for general use | More recommend for activities with higher frequency content
Less expensive | More expensive

## Slide 53
2. SYSTEM ELEMENTS
Figure 3. Positioning of the dynamometric platforms in the center of the walkway.
2.1 The Platform
Configuration on the ground
Steps of acceleration
Steps of deceleration
Platform

## Slide 54
2. SYSTEM ELEMENTS
Figure 4. Configuration of two dynamometric platforms. (Left) Basic configuration for gait analysis. (Right) Basic configuration for different functions.
2.1 The Platform
Configuration on the ground
Platform 1
Platform 2
Platform 1
Platform 2

## Slide 55
2. SYSTEM ELEMENTS
Figure 5. Optimal configuration with four dynamometric platform for gait analysis and another functions.
2.1 The Platform
Configuration on the ground
Platform 3
Platform 4
Platform 1
Platform 2

## Slide 56
2. SYSTEM ELEMENTS
Figure 6. Configuration with four dynamometric platforms for gait analysis in children with neurological disorders..
2.1 The Platform
Configuration on the ground
Platform 3
Platform 4
Platform 1
Platform 2
Platform 1
Platform 2
Platform 3
Platform 4

## Slide 57
2. SYSTEM ELEMENTS
2.2 The Software
Registration of ground reaction forces and the subsequent editing of the data
Control of gait velocity
Management of more than one instrumental technique at the same time

## Slide 58
3. ASSESSMENT PROTOCOL
CALIBRATION
ANTHROPOMETRIC DATA
DATA CAPTURE
REVIEW OF THE TRIALS
OBTAINING RESULTS

## Slide 59
Procedure that indicate the system when there is no load. Signal to zero.
3.1. CALIBRATION OF THE EQUIPMENT
Reset procedure
Avoid possible signal drift
No load
Figure 7. Force platform without load for calibration procedure..

## Slide 60
Anthropometric data are crucial to describe the participants in a study or make comparisons between groups.
3.2. ANTHROPOMETRIC DATA RECORDING
Weight of the person evaluated is important to use the ground reaction forces registered in posterior comparisons between-group analysis.
Figure 8. Weight registration on a dynamometric platform prior to gait analysis.
Normalization of the forces

## Slide 61
3.3. DATA CAPTURE PROCEDURE
1
With or without shoes
2
Delimited walkway
3
Standardization of the instruction
Gait velocity control
4
Valid registration
5
Number of the repetitions
6

## Slide 62
With or without shoes
3.3. DATA CAPTURE PROCEDURE
Figure 9. Gait assessment modalities with dynamometric platform.

## Slide 63
3.3. DATA CAPTURE PROCEDURE
Delimited walkway
Figure 10. Delimited walkway from gait assessment with dynamometric platform. (Right) Space that allows acceleration before to the step within the platform. (Left) Space for deceleration after stepping on the platform.

## Slide 64
3.3. DATA CAPTURE PROCEDURE
Standardization of the instruction
Walk in a straight line from one mark to another when the "start" indication is given
Walk looking forward
Walk without any kind of supports to avoid transmitting the force to another point
Walk at a comfortable, usual or self-selected speed
Walk looking forward

## Slide 65
3.3. DATA CAPTURE PROCEDURE
Valid registration
Figure 11. Gait assessment with dynamometric platform. (Left) Valid repetition. (Middle) Invalid registration due to the interference of the previous step. (Right) Invalid registration due to the interference of the next step.

## Slide 66
3.3. DATA CAPTURE PROCEDURE
Number of the repetitions
Figure 12. Curves of ground reaction forces. Red: vertical force. Blue: anterior-posterior force. Green: mediolateral force. (Left) Evaluation that includes a single record of reaction forces for right and left foot. (Right) Evaluation that includes several records for right and left foot.

## Slide 67
3.3. DATA CAPTURE PROCEDURE
Gait velocity control
1.14 m/s
1.60 m/s
1.30 m/s
1.60 m/s
Figure 13. Curves of ground reaction forces at different gait speed (m/s, meter per second). In each graph, the magnitude of the force (N, Newton) is shown on the Y axis and the time (s) on the X axis.

## Slide 68
Check the speed differences of each gait repetition
3.4. REVIEW OF THE REPETITIONS COLLECTED
Remove curves with morphology clearly different from most recorded curves
Abnormal capture
Abnormal capture
Figure 14. Examples of gait assessment with dynamometric platforms. In both graphs the participant suffers an involuntary ankle inversion.

## Slide 69
Force that acts on a body as a result of the body resting on the ground or hitting the ground, as it can be during the bipedal position and during the movement, like the human gait.
3.5. READING THE RESULTS OBTAINED
Ground Reaction Forces (GRF)
Centre of Pressure (COP)
The position on the floor of the ground reaction force vectors is known as the Centre of pressure.
The COP refers to the average pressure point beneath the foot or feet.
Figure 15. Ground reaction force vector.

## Slide 70
The ground reaction force components
3.5. READING THE RESULTS OBTAINED
Vertical force (Fz)
Anterior-posterior force (Fy)
Medial-lateral force (Fx)
Forces (Newton)
Percentage of stance phase (%)
Figure 16. Ground reaction force and its three components.

## Slide 71
The ground reaction force: Vertical component
3.5. READING THE RESULTS OBTAINED
VERTICAL VECTOR OF GRF (N)
Fz 1: Peak force in maximal weight acceptance
Fz 2: Peak
force in mid stance
Fz 3: Peak force in push-off
Fz1
Fz2
Fz3
Time to Fz1
Time to Fz2
Time to Fz3

## Slide 72
ANTERIOR-POSTERIOR VECTOR OF GRF (N)
The ground reaction force: Anterior-posterior component
3.5. READING THE RESULTS OBTAINED
Fy 1: Maximum posterior force. Correspond to the breaking
Fy 2: Maximum anterior force
Fy1
Fy2
Cross over
Time to Fy1
Time to Fy2
Time to cross over
Posterior
Impulse
Anterior
Impulse

## Slide 73
The ground reaction force: Medial-lateral component
3.5. READING THE RESULTS OBTAINED
MEDIAL-LATERAL VECTOR OF GRF (N)
Fx 1: Maximum lateral force
Fx 1
Fx 2
Fx 3
Lateral
Medial
Fx 2: Maximum loading medial force
Fx 3:
Maximum propulsion medial force

## Slide 74
The Centre of pressure (COP)
3.5. READING THE RESULTS OBTAINED
Figure 17. Centre of pressure movement during gait at slow (dashed line) and fast velocity (solid line) . From Todd C. Pataky et al. 2014.
Trajectory in the X and Y axes
Medial-lateral movement
Anterior-posterior movement
Medial-lateral against Anterior-posterior
COP speed against Time (stance phase)

## Slide 75
Pedotti diagram
3.5. READING THE RESULTS OBTAINED
Figure 18. Pedotti diagram. Each arrow represent de ground reaction vector at each point of the stance phase, the base of each vector being the centre of pressure at that point in time. Image from Clinical Movement Analysis, Vrije Universiteit. Available: www.studeersnel.nl.

## Slide 76
The momentum on a force plate
3.5. READING THE RESULTS OBTAINED
Figure 19. Momentum on the platform during the stance phase of a healthy subject gait assessment.
Not directly measurable
Can be calculated with the location of the centre of the platform in the medial-lateral and anterior-posterior directions

## Slide 77
No instrumentation is required
Ease of use and interpretation of results
Precise measuring equipment
Development of portable platforms
4 ADVANTAGES AND DISADVANTAGES
Advantages
Disadvantages
It should be built on the walkway
The number of different contact surfaces to be measured is limited
Need for more than one platform
High economic cost

## Slide 78
D.1 Which gait biomechanical instruments evaluation protocols exist?
Part 4. Instrumented pressure insoles and gait assessment.
Clinical approach

## Slide 79
Kinetic analysis technique
Insoles with pressure sensors
In-shoes pressure system
Portable equipment
Gait assessment in functional
conditions
Importance of measuring pressure
1. DEFINITION
Instrumented insoles for
plantar pressure
Figure 1. Instrumented insoles
with pressure sensors.

## Slide 80
2. SYSTEM ELEMENTS
The insoles with pressure sensors
A signal amplifier
A wireless transmitter module
Software (and computer)
Figure 2. Elements of a plantar pressure measurement system based on instrumented insoles. Biofoot/Biomechanics Institutes of Valencia system.

## Slide 81
2. SYSTEM ELEMENTS
Figure 3. Pressure sensor distribution in instrumented insole.
Instrumented insoles
Types of sensors
Different sizes
  Avoid folds
  Sensor distribution
Pressure unit: kPa
Careful maintenance

## Slide 82
2. SYSTEM ELEMENTS
Instrumented insoles: types of sensors
A
B
C
Figure 4. Functioning of pressure sensors. (A) Capacitive. (B) Resistive. (C) Piezoelectric. Images from Nader Ahmadzadeh et al. 2016.
Capacitive
Measurement changes in electrical capacitance
Resistive
Measurement the change in electrical resistance
Piezoelectric
Measurement the voltage from the applied pressure to a material

## Slide 83
2. SYSTEM ELEMENTS
Figure 5. Pressure
plantar measurement
system.
Instrumented insoles and elements

## Slide 84
2. SYSTEM ELEMENTS
Technical specifications and recommendations for gait
Number of sensors per insole
Sampling frequency (Hz)
Pressure range (kPa)
24 – 1000 sensors per insole
Critical zones
Number of samples the system is capable of measuring per second
For gait: 50-100 Hz
Range of pressure capable of measuring
Normal gait: 200-500 Hz
Diabetic neuropathology 1000-3000 Hz
Figure 6. Foot anatomical areas that support the major body-weight. Image from Lin Shu et al. 2010.

## Slide 85
Insoles selection and instrumentation
Suitable insole
“not too tight or loose”
Subject seated
Closed shoe
3. ASSESSMENT PROTOCOL
Figure 7. Insoles positioning.
Biofoot/Biomechanics Institutes of Valencia system.

## Slide 86
Intrumented insoles calibration
Necessary to avoid drift signal
Calibration of pressure sensors across system varies considerably
  Standing with the weight of the subject
  Sitting
System with piezoelectric sensors: Period for temperature and humidity adaptation inside footwear
3. ASSESSMENT PROTOCOL
Figure 8. Position for calibration procedure.

## Slide 87
Control of gait speed
3. ASSESSMENT PROTOCOL
The magnitudes of the forces generated when walking depend on several factors, including speed
In an evaluation of plantar pressures, the speed performed must be controlled
An increase in walking speed causes an increase in pressures under the foot
Confortable speed gait
Slow
Fast
Speed variations between trials of the same condition: no more than 10%

## Slide 88
Obtaining the results
3. ASSESSMENT PROTOCOL
Pressure =
Force
Area
Figure 9. Colour scale map from a plantar pressure assessment.
Low
pressure
High
pressure
Definition of pressure
Colour scale

## Slide 89
Obtaining the results
3. ASSESSMENT PROTOCOL
Figure 10. Study of plantar pressures per area of the foot. In order from left to right: medial area, external area, heel, midfoot and forefoot. Image from User manual, Biofoot/Biomechanics Institutes of Valencia system
Regions of interest
Average pressure
Peak pressure

## Slide 90
Obtaining the results
3. ASSESSMENT PROTOCOL
Figure 11. Pressure-time integral curve. Image from Richards J. (2018) The Comprehensive Textbook of Clinical Biomechanics. 2nd ed.
.
Pressure-Time Integral
Centre of pressure
Other spatiotemporal parameters.

## Slide 91
4 ADVANTAGES AND DISADVANTAGES
Advantages | Disadvantages
Allow the direct measurement of pressure acting on the foot | The curvature of the foot
Assessment in functional conditions: in movement and with shoes | The lack of space for the transducers
 | The use of wires from the inside of the shoe
It does not require excessive preparation of the subject | Is not recommended to compare pressure measurement values between different system

## Slide 92
D.1 Which gait biomechanical instruments evaluation protocols exist?
Key Ideas

## Slide 93
KEY IDEAS
Human gait can be evaluated with different biomechanical assessment instruments, which allow us to objectify its performance and deficits.
Photogrammetry is a technique for measuring kinematic variables from images, either from photo cameras or video cameras.
To perform a gait analysis with photogrammetry, it is necessary to instrument the person evaluated with a biomechanical model composed of markers that will indicate the points that make up the body segments that perform the movement
The most used biomechanical model to measure gait is the Calibrated Anatomical System Technique (CAST), which allows to analyze the march in the three planes of movement.

## Slide 94
KEY IDEAS
Among the clinical gait variables that can be measured with photogrammetry are Range of flexion-extension movement, internal-external rotation, abduction-adduction in each joint of the biomechanical model and Peak angles, which refers to the maximum degree of movement reached in the analyzed curve.
Linear acceleration during gait is possible to measure with an accelerometer system and is refers to the change in the linear velocity over successive time intervals. The unit of acceleration, in the International System of Unit, is meters per second square (m/s2) although it can often be found expressed in gravity ratio (g). Positive acceleration have a positive value, but a negative value represents a deceleration.
The protocol using accelerometers in gait analysis typically consists of attaching an accelerometer to the trunk, head and tibial segment. One of the most important points of the protocol is the fixation of the accelerometer on the skin, which must prevent the relative movement of the accelerometer to faithfully represent the acceleration of the segment to be measured.

## Slide 95
KEY IDEAS
A force platform or a force plate is an equipment to measure ground reaction forces (GRF) and their point of application known as centre of pressure (COP). It is an element widely used in the assessment of human gait and balance, as well as in a several human activities and functions.
The registered forces will depend, as we have already said, on the speed, but also on the weight of the valued person. That is why, in order to make comparisons between individuals we need to divide the forces obtained by the weight of the person and thus obtain a comparable dimensionless parameter between subjects. On the other hand, the control of gait speed is also necessary between gait trials of the same condition.
The ground reaction force vector has three component, in the three axes of space: a) Vertical force component in the Z axis, b) Anterior-posterior force in the Y axis, and, c) Medial-lateral component in the X axis.

## Slide 96
KEY IDEAS
The instrumented insoles for plantar pressure are a kinetic analysis technique that, inside the insoles have a several of pressure sensors strategically distributed, to measure the static and dynamic plantar pressure. These insoles are located inside the footwear of the person evaluated, so it is a portable equipment and allow the assessment of gait in functional conditions, it is mean, with footwear and in movement. The importance of measuring plantar pressure is that excessive pressures can cause tissue damage.
In the analysis of plantar pressures, it is more useful to study the parameters for each area of the foot. Usually the devices allow to analyze the results of the plantar pressure divided in the heel, midfoot, forefoot and internal and external area of the foot.

## Slide 97
D.1 Which gait biomechanical instruments evaluation protocols exist?
Bibliography

## Slide 98
Ali Salah A., Gevers T., Editors. Compute Analysis of Human Behavior. 1st ed. London (England): Springer, 2011.
Armand, S., Decoulon, G., Bonnefoy-Mazure, A. (2016) Gait analysis in children with cerebral palsy. EFORT Open Rev, 1.
Bauer, JJ., Pavol, MJ., Snow, CM., Hayes, WC. (2007) MRI-derived body segment parameters of children differ from age-based estimates derived using photogrammetry. Journal of Biomechanics, 40, 2904-2910. doi:10.1016/j.jbiomech.2007.03.006.
Cappozzo, A., Croce, U. D., Leardini, A., Chiari, L. (2005). Human movement analysis using stereophotogrammetry Part 1: theoretical background. Gait & Posture, 21(2), 186–196. doi:10.1016/j.gaitpost.2004.01.010
Chiari, L., Croce, U. D., Leardini, A., Cappozzo, A. (2005). Human movement analysis using stereophotogrammetry Part 2: Instrumental errors. Gait & posture, 21(2), 197-211. doi:10.1016/j.gaitpost.2004.04.004
Croce, U. D., Leardini, A., Chiari, L., Cappozzo, A. (2005). Human movement analysis using stereophotogrammetry Part 4: assessment pf anatomical landmark misplacement and ist effects on joint kinematics. Gait & posture, 21(2), 226-237. doi:10.1016/j.gaitpost.2004.05.003.
Leardini, A., Chiari, L., Croce, U. D., & Cappozzo, A. (2005). Human movement analysis using stereophotogrammetry Part 3. Soft tissue artifact assessment and compensation. Gait & Posture, 21(2), 212-225. doi:10.1016/j.gaitpost.2004.05.002
Lee, EH., Goh, JC., Bse K. (1992) Value of gait analysus in the assessment of surgery in cerebral palsy. Arch Phys Med Rehabil, 73(7), 642-6.
5. BIBLIOGRAPHY

## Slide 99
Lu, T.-W., & Chang, C.-F. (2012). Biomechanics of human movement and its clinical applications. The Kaohsiung Journal of Medical Sciences, 28(2), S13–S25. doi:10.1016/j.kjms.2011.08.004
Monk A. P. , Van Oldernrijk J. , Riley Nicholas D. , Gill H.S., Murray D. W. (2016). Biomechanics of the lower limb. Surgery, 34(9), 427-435. doi:10.1016/ j.mpsur.2016.06.007
Pueo, B., Jimenez-Olmedo JM. (2017). Application of motion capture technology for sport performance analysis. El uso de la tecnología de captura de movimiento para el análisis del rendimiento deportivo. Retos, 32(2), 241-247.
Pantzar-Castilla, E., Cereatti, A., Figari, G., Valeri, N., Paolini, G., Della Croce, U., Magnuson, A., Riad, J. (2018) Knee joint sagittal plane movement in cerebral palsy: a comarative study of 2-dimensional markerless video and 3-dimensional gait analysis. Acta Orthopaedica, 89(6), 656-661. DOI 10.1080/17453674.2018.1525195.
Richards J., Editor. The Comprehensive Textbook of Clinical Biomechanics. 2nd ed. Preston (UK): Elsevier, 2018.
Sandau, M., Koblauch, H., Moeslund, T. B., Aanæs, H., Alkjær, T., & Simonsen, E. B. (2014). Markerless motion capture can provide reliable 3D gait kinematics in the sagittal and frontal plane. Medical Engineering & Physics, 36(9), 1168–1175. doi:10.1016/j.medengphy.2014.07.007
Schenk, T. (2005). Introduction to photogrammetry. The Ohio State University, Columbus, 106.
Zuk, M., Pezowicz, C. (2015) Kinematic Analysis of a Six-Degrees-of-Freedom Model Based on ISB Recommendation: A Repeatability Analysis and Comparison with Conventional Gait Model. Applied Bionics and Biomechanics, 503713. doi: 10.1155/2015/503713.
5. BIBLIOGRAPHY

## Slide 100
Brodie M., Beijer T., Canning C. and Lord S. Head and pelvis stride-to-stride oscillations in gait: validation and interpretation of measurements from wearable accelerometers. Physiol. Meas. 36 (2015) 857–872.
Godfrey A., Del Din S., Barry G., Mathers J.C., and Rochester L. Instrumenting gait with an accelerometer: A system and algorithm examination. Med Eng Phys. 2015 Apr; 37(4): 400–407.
Jarchi D., Pope J., Lee T.K. M., Tamjidi L., Mirzaei A. and Sanei S. A review on accelerometry based gait analysis and emerging clinical applications. EEE Rev. Biomed. Eng., vol. 11, pp. 177–194,2018.
Lafortune M. Three-dimensional acceleration of the tibia during walking and running. J. Biomechanics Vol. 24, Nº 10, pp. 877-886, 1991.
Richards J., Editor. The Comprehensive Textbook of Clinical Biomechanics. 2nd ed. Preston (UK): Elsevier, 2018.
Salah A., Gevers T., Editors. Compute Analysis of Human Behavior. 1st ed. London (England): Springer, 2011.
Sant’Anna A., Wickstrin N. Developing a Motion Language: Gait Analysis from accelerometers sensor systems. 3rd International Conference on Pervasive Computing Technologies for Healthcare, London, 1-3 April, 2009, pp. 1-8. 108 (2012) 715-723.
5. BIBLIOGRAPHY

## Slide 101
Sinclair J., Hobbs S., Protheroe L., Edmundson C., Greenhalgh A. Determination of gait events using an externally mounted shank accelerometer. Journal of Applied Biomechanics, 2013, 29, 118-122.
Woodford, Chris. Accelerometers. [cited 2020 January]. Web site available: https://www.explainthatstuff.com/accelerometers.html.
Tao W., Liu T., Zheng R., Feng H. Gait Analysis Using Wearable Sensors. Sensors 2012, 12(2), 2255-2283.
Yang M., Zheng H., Wang H. McClean S., Newell D. iGait: An interactive accelerometer based gait analysis system. Compute methods and programs in biomedicine 108 (2012) 715-723.
5. BIBLIOGRAPHY

## Slide 102
Ali Salah A., Gevers T., Editors. Compute Analysis of Human Behavior. 1st ed. London (England): Springer, 2011.
Azadian E., Majlesi M., Jafarnezhadgero A.A. The effect of working memory intervention on the gait patterns of the elderly. Journal of Bodywork & Movement Therapies 22 (2018) 881e887.
Claudiane Arakaki Fukuchi, Reginaldo Kisho Fukuchi and Marcos Duarte. Effects of walking speed on gait biomechanics in healthy participants: a systematic review and meta-analysis. Systematic Reviews (2019) 8:153.
G. Ryckewaert, A. Delval, S. Bleuse, J.-L. Blatt, L. defebvre. Biomechanical mechanisms and centre of pressure trajectory during planned gait termination. Neurophysiologie Clinique/Clinical Neurophysiology (2014) 44, 227—233.
Hadar Shauliana, Deborah Solomonow-Avnona, Amir Hermanb, Nimrod Rozenc, Amir Haima, Alon Wolfa. The effect of center of pressure alteration on the ground reaction force during gait: A statistical model. Gait & Posture 66 (2018) 107–113.
Lucia Bizovska, Zdenek Svoboda, Patrik Kutilek, Miroslav Janura, Ales Gaba. Variability of centre of pressure movement during gait in young and middle-aged women. Gait & Posture 40 (2014) 399–402.
5. BIBLIOGRAPHY

## Slide 103
Moon-Seok Kwon, Yu-Ri Kwon, Yang-Sun Park, Ji-Won. Comparison of gait patterns in elderly fallers and non-fallers. Technology and Health Care 26 (2018) S427–S436.
Richards J., Editor. The Comprehensive Textbook of Clinical Biomechanics. 2nd ed. Preston (UK): Elsevier, 2018.
Sánchez J., Prat J., Hoyos J., Viosca E., Soler C., Comín M., Lafuente R., Cortés A., Vera P. Biomecánica de la marcha normal y patológica. Valencia, España: Instituto de Biomecánica de Valencia, 1993.
Sławomir Winiarski, Alicja Rutkowska-Kucharska. Estimated ground reaction force in normal and pathological gait. Acta of Bioengineering and Biomechanics Vol. 11, No. 1, 2009.
Todd C. Pataky, Mark A. Robinson , Jos Vanrenterghem, Russell Savage, Karl T. Bates, Robin H. Crompton. Vector field statistics for objective center-of-pressure trajectory analysis during gait, with evidence of scalar sensitivity to small coordinate system rotations. Gait & Posture 40 (2014) 255–258.
Vipul Lugade and Kenton Kaufman. Center of Pressure Trajectory during Gait: A Comparison of Four Foot Positions. Gait Posture. 2014 May ; 40(1): 252–254.
Zdenek Svoboda, Lucia Bizovska, Miroslav Janura, Eliska Kubonova, Katerina Janurova, Nicolas Vuillerme. Variability of spatial temporal gait parameters and center of pressure displacements during gait in elderly fallers and nonfallers: A 6-month prospective study. PLoS One. 2017 Feb 27;12(2):e0171997.
5. BIBLIOGRAPHY

## Slide 104
Béseler M.R., Grao C.M., Gil Á. y Martínez Lozano M.D.. Valoración de la marcha mediante plantillas instrumentadas en pacientes con espasticidad de miembros inferiores tras infiltración con toxina botulínica. Neurología. 2012;27(9):519—530.
Brus S.A, Waaijman R. The value of reporting pressure–time integral data in addition to peak pressure data in studies on the diabetic foot: A systematic review. Clin Biomech (Bristol, Avon). 2013 Feb;28(2):117-21.
Dyer Philip S. and Morris Stacy J. Bamberg. Instrumented Insole vs. Force Plate: A Comparison of Center of Plantar Pressure. Conf Proc IEEE Eng Med Biol Soc. 2011;2011:6805-9.
Instituto de Biomecánica de Valencia (IBV). Biofoot/IBV Manual de Usuario. Séptima versión. Valencia, España: Instituto de Biomecánica de Valencia, 2012.
Lin Shu, Tao Hua, Yangyong Wang, Qiao Li, David Dagan Feng, and Xiaoming Tao. In-Shoe Plantar Pressure Measurement and Analysis System Based on Fabric Pressure Sensing Array. IEEE Trans Inf Technol Biomed. 2010 May;14(3):767-75.
Martínez A., Sánchez Ruiza, M. Barrés Carsíb, C. Pérez Lahuerta, A. Guerrero Alonsoc y C. Soler Gracia. A new diagnostic and therapeutic diagnostic method of the foot disease based on biofoot/ibv instrumented insoles. Rehabilitación Vol. 37. Núm. 5. Páginas 240-251 (Enero 2003).
5. BIBLIOGRAPHY

## Slide 105
Martínez-Nova A., Sánchez-Rodríguez R., Cuevas García J.C. Patrón de presiones plantares en el pie normal: Análisis mediante sistema Biofoot de plantillas instrumentadas. El Peu 2006;26(4):190-194.
Martínez-Novaa A., Cuevas-Garcíaa J.C., Sánchez-Rodrígueza R., Pascual-Huertab J., Sánchez-Barrado E. Study of plantar pressure patterns by means of instrumented insoles in subjects with hallux valgus. Revista Española de Cirugía Ortopédica y Traumatología (English Edition). Volume 52, Issue 2, March–April 2008, Pages 94-98.
Martínez-Nova A., Sánchez-Rodríguez R., Leal-Muro A., Pedrera-Zamorano J.D. Dynamic Plantar Pressure Analysis and Midterm Outcomes in Percutaneous Correction for Mild Hallux Valgus. J. Orthop Res. 2011 Nov;29(11):1700-6.
Nurul Amziah, Yunus, Izhal Abdul Halin, Nasri Sulaiman, Noor Faezah Ismail, Ong Kai Sheng. Valuation on MEMS Pressure Sensors and Device Applications. World Academy of Science, Engineering and Technology International Journal of Electronics and Communication Engineering Vol:9, No:8, 2015.
Richards J., Editor. The Comprehensive Textbook of Clinical Biomechanics. 2nd ed. Preston (UK): Elsevier, 2018.
Wertsch J., Webster J., Tompkins W. A portable insole plantar pressure measurement system. Journal of Rehabilitation Research and Development Vol. 29 No. 1,1992 Pages 13-18.
5. BIBLIOGRAPHY

## Slide 106
The European Commission's support for the production of this publication does not constitute an endorsement of the contents, which reflect the views only of the authors, and the Commission cannot be held responsible for any use which may be made of the information contained therein